## Slide 1: Overview of Computer Networks
P. Krishna Reddy, IIIT Hyderabad

## Slide 3: Topics completed: Operating system
Input: hardware
Output is system calls to develop applications
Objectives: to improve throughput and response time, deadlines, waiting time

## Slide 4: Outline
Introduction
Data link layer: An overview
Medium Access layer: An overview
Network layer: An overview
Transport layer: An overview

## Slide 5: Networking
Input: thousands of computers connected through communication channels
Output is primitives to develop applications
Objectives: to improve throughput, reliability, and response time, deadlines, waiting time
Networking Applications (http, sendmail,…)
Tens of thousands of computers and devices connected through communication channels distributed across the world (thousands of kilometers
Networking Protocols to implement system calls with code (Interface)

## Slide 6: How it is different from producer and consumer problem?
Producer places an item and consumer consumes an item from the buffer.
Normally in the same computer
Producer waits if the buffer is full, consumer waits if buffer is empty.
How to enable producer and consumer to exchange data, suppose a video if
  Producer is in one computer
  Consumer is another computer
Connected through long communication channel (thousands of kilometers) with intermediate links and junctions
Issues
  Links might not be reliable
  All the data may not be delivered
  So, more mechanisms are needed.
Requires
  Error control mechanisms
  Flow control mechanisms

## Slide 7: Introduction
18th century is dominated by mechanical systems
19th century is the age of steam engine
20th century- Information Technology
  Information gathering processing and distribution
  Others: radio, television, telephones, communication satellites and Internet
Computer network
  Large number of separate but interconnected computers.
Distributed system: A collection of independent computers which appears to users as single coherent system. Another layer such as world wide web is presented on the top of computer network
In computer network, users are exposed to machines.

## Slide 8: Users of computer networks
Business applications
  Resource sharing
  To make programs, equipment, and data available to anyone on the network without regard to the location of the user.
  Almost every office requires computer networks

## Slide 9: Home Applications
Homes contain many networked devices, e.g., computers, TVs, connected to the Internet by cable, DSL, wireless, etc.
Home users communicate, e.g., social networks, consume content, e.g., video, and transact, e.g., auctions
  Wikipedia, facebook, twitter, sms, IP television
Some application use the peer-to-peer model in which there are no fixed clients and servers:
In a peer-to-peer system there are no fixed clients and servers.

## Slide 10
Some forms of e-commerce.
Tag | Full name | Example
B2C | Business-to-consumer | Ordering books online
B2B | Business-to-business | Car manufacturer ordering tires from supplier
G2C | Government-to-consumer | Government distributing tax forms electronically
C2C | Consumer-to-consumer | Auctioning second-hand products online
P2P | Peer-to-peer | Music sharing

## Slide 11: Mobile Users
Tablets, laptops, and smart phones are popular devices; WiFi hotspots and 3G cellular provide wireless connectivity.
Mobile users communicate, e.g., voice and texts, consume content, e.g., video and Web, and use sensors, e.g., GPS.
Sensor networks
Wireless and mobile are related but different:

## Slide 12: Social Issues
Network neutrality – no network restrictions
Content ownership, e.g., DMCA (Digital Millennium Copy right Act) takedowns
Anonymity and censorship
Privacy, e.g., Web tracking and profiling
Theft, e.g., botnets and phishing

## Slide 13: Network Hardware
Networks can be classified by their scale:
Scale | Type
Vicinity | PAN (Personal Area Network) »
Building | LAN (Local Area Network) »
City | MAN (Metropolitan Area Network) »
Country | WAN (Wide Area Network) »
Planet | The Internet (network of all networks)

## Slide 14: About networking technology
Two dimensions
  Transmission technology
  Scale
Two types of transmission technology
  Broadcast links
  Point to point links
Point-to-Point links
  One sender and one receiver
  Connect individual pairs of links
  They may have to visit some intermediate machines.
Broadcast link
  Communication link is shared by several machines
  A packet is received by all machines. The address in the packet specified intended recipient.
  Broadcasting: message is sent to all machines
  Multicasting: message is sent to a subset of nodes.

## Slide 15: Layered model
Layered model
  Divide the roles/issues among layers
Develop each layer
  Lower layer provides services to higher layer.

## Slide 16: Protocol Layers
Protocol layering is the main structuring method used to divide up network functionality.
Each protocol instance talks virtually to its peer
Each layer communicates only by using the one below
Lower layer services are accessed by an interface
At bottom, messages are carried by the medium

## Slide 17
Protocol Layers (2)
Example: the philosopher-translator-secretary architecture
Each protocol at different layers serves a different purpose

## Slide 18: Protocol Layers
Each lower layer adds its own header (with control inform- ation) to the message to transmit and removes it on receive
Layers may also split and join messages, etc.

## Slide 19: Connection-Oriented vs. Connectionless
Service provided by a layer may be kinds of either:
Connection-oriented, must be set up for ongoing use (and torn down after use), e.g., phone call
Connectionless, messages are handled separately, e.g., postal delivery

## Slide 20: Service Primitives (or system calls)
A service is provided to the layer above as primitives
Hypothetical example of service primitives that may provide a reliable byte stream (connection-oriented) service:

## Slide 21: Service Primitives
Hypothetical example of how these primitives may be used for a client-server interaction
Client Server
LISTEN (0)
RECEIVE
CONNECT (1)
Connect request
Accept response Request for data
ACCEPT (2)
SEND (4)
RECEIVE
SEND (3)
DISCONNECT (5)
Reply Disconnect
DISCONNECT (6)
Disconnect

## Slide 22: Relationship of Services to Protocols
Recap:
A layer provides a service to the one above [vertical]
A layer talks to its peer using a protocol [horizontal]

## Slide 23: Reference Models
Reference models describe the layers in a network architecture
OSI reference model »
TCP/IP reference model »
Model used for this text »
Critique of OSI and TCP/IP »

## Slide 24: OSI (Open Systems Interconnection) Reference Model
A principled, international standard, seven layer model to connect different systems
Provides functions needed by users Converts different representations
Manages task dialogs
Provides end-to-end delivery
Sends packets over multiple links
Sends frames of information
Sends bits as signals
ISO OSI: International Standards Organization Open Systems Interconnection

## Slide 25: About Layers
The Physical layer
  Transmitting raw bits over a communication channel
  One side sends 1/0 and the other side receives 1/0
  Issue: What electrical signals should be used?
  Design issues
    Mechanical, electrical and timing interfaces
The Data Link Layer
  Transform a raw transmission facility into a like that appears free of undetected transmission errors.
  Data frame and ack. Frame
  Interface between fast transmitter and slow receiver
  Broadcast networks: How to control access to shared channel?
    LAN
The network layer
  Controls the operation of the subnet.
  Issue: how packets are routed from source to destination?
  Resolving bottlenecks; concession control
  In broadcast networks, network layer is absent

## Slide 26: About Layers
The Transport layer
  Accept data split into small units, if required, and pass it to network layer.
  It isolates upper layer with the possible changes in the hardware technology.
  It also determines the type of service: connection oriented or connectionless.
  It is an end to end layer
  One computer talks with other computer
  In the lower layers the communication is between the source and intermediate computer.
The Session Layer
  Helps to establish sessions
  Dialog control, token management, synchronization
The presentation layer
  Syntax and semantics of the information
  It allows computers with different data representations to communicate
The application layer
  Set of protocols
  Popular one is HTTP (Hypertext transfer protocol)
  File transfer
  Electronic mail
  Network news

## Slide 27
The OSI reference model.

## Slide 28: TCP/IP Reference Model
A four layer model derived from experimentation; omits some OSI layers and uses the IP as the network layer.
“ ”
TCP/IP stands for Transmission Control Protocol/Internet Protocol and is a suite of
communication protocols used to interconnect network devices on the internet.
The TCP/IP model with some protocols we will study.
ICMP: Internet Control Message Protocol
UDP: User Datagram Protocol
DSL: Digital subscriber line
SONET: Synchronous Optical Network
SMTP: Simple Mail Transfer Protocol
RTP: Realtime transport protocol
DNS: Domain name system

## Slide 29
The TCP/IP reference model.

## Slide 30
TCP/IP model
It is based on the TCP/IP model but we call out the physical layer and look beyond Internet protocols.

## Slide 31: Internet
The modern Internet is more complex:
ISP networks serve as the Internet backbone
ISPs connect or peer to exchange traffic at IXPs
Within each network routers switch packets
Between networks, traffic exchange is set by business agreements
Customers connect at the edge by many means
− Cable, DSL, Fiber-to-the-Home, 3G/4G wireless, dialup
Data centers concentrate many servers (“the cloud”)
Most traffic is content from data centers (esp. video)
The architecture continues to evolve

## Slide 32: Internet
Architecture of the Internet
DSLAM (Digital Subscriber Line Access Multiplexer)
Fiber to the home (FTTH)
A cable modem termination system (CMTS)
Internet eXchange Point (IXP) : Internet Exchange Point (IXP) can earn money by charging each ISP that connects to it. The IXP charges each ISP based on the amount of traffic sent to or received from the IXP.

## Slide 33: Outline
Introduction
Data link layer: An overview
Medium Access layer: An overview
Network layer: An overview
Transport layer: An overview

## Slide 34: The Datalink Layer
How to transmit information between two adjacent machines in a reliable and efficient manner?
  Conceptually two machines are connected like a wire (coaxial cable, telephone line, or wireless channel)
  There is a non-zero propagation delay
  Communication channel makes errors

## Slide 35: The Data Link Layer
Application Transport
Responsible for delivering frames of information over a single link
Handles transmission errors and regulates the flow of data
Provides well-defined service to network layer
Dealing with transmission errors
Regulates data between high-speed sender and slow speed receiver
Network Link Physical

## Slide 36: Frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Network
Link
Virtual data path
Actual data path
Physical

## Slide 37: Possible Services
Unacknowledged connectionless service
Frame is sent with no connection / error recovery
Ethernet is an example
Acknowledged connectionless service
Frame is sent with retransmissions if needed
Example is 802.11 (WiFi)
Acknowledged connection-oriented service
  First phase: Connection is set-up
  Second phase: Frames are transmitted
  Third phase: connection is released.

## Slide 38: Algorithms
Framing method
  Bit stuffing
Error control
  Error detection and correction
  Checksum-based protocols
Flow control
  Sliding window protocols.

## Slide 39: Sliding Window Protocols
Summary of sliding window protocols
  Sender maintains a sequence numbers for frames (sending window)
  Receiver also maintains a receiving window.
  Whenever a packet is received from network layer, it gives a highest sequence number and the upper edge of the window is advanced by one.
  When ack, arrives lower edge of the window is advanced by one.
  Sender needs n buffers to hold unack frames

## Slide 40: Outline
Introduction
Data link layer: An overview
Medium Access layer: An overview
Network layer: An overview
Transport layer: An overview

## Slide 41: The Medium Access Control Sublayer
Networks links can be divided into two categories:
  Point-to-point connections
    WAN is point-to-point links
  Broadcast channels/multiaccess channels or random access channels
    For fixed channel and traffic from N users
    Wireless is a broadcast channel
  Analogy
    Conference call with six people with different telephones
Medium access control sublayer is a sublayer in data link layer
Multi-access channels and LANs are closely related
MAC sublayer is the bottom of the datalink layer

## Slide 42: The MAC Sublayer
Application Transport
Responsible for deciding who sends next on a multi-access link
An important part of the link layer, especially for LANs
Network Link Physical
MAC is in here!

## Slide 43: Classic Ethernet (1) – Physical Layer
One shared coaxial cable to which all hosts attached
Up to 10 Mbps, with Manchester encoding
Hosts ran the classic Ethernet protocol for access

## Slide 44: Carrier Sense Multiple Access (CSMA)
CSMA (Carrier Sense Multiple Access) improves on ALOHA by sensing the channel!
User doesn’t send if it senses someone else
Variations on what to do if the channel is busy:
1-persistent (greedy) sends as soon as idle
Nonpersistent waits a random time then tries again
p-persistent sends with probability p when idle

## Slide 45: 1-Persistent CSMA Protocol
When a station has data to send, it listens to the channel
If the channel is idle, the station sends the data
If the channel is busy, the station waits until it becomes idle.
If the collision occurs, the station waits for random amount of time and starts over again.
It is called 1-persistent, because, the station transmits with a probability of 1 when it finds the channel idle.
Issues: when two stations ready, collisions occur, if they are not so impatient.

## Slide 46: CSMA/CD: CSMA with Collision Detection
In CSMA, if two stations sense a channel to be idle and begin transmitting, the signals will collide.
Alternative: Stations quickly detect collision and abruptly stop transmitting.
  It saves time and bandwidth
If a station detects collision, it aborts its transmission, waits a random period of time and tries again.
CSMA/CD consists of alternating contention and transmission periods and idle periods (when all stations are quiet).
If the channel transmits 2*t, whether t is the signal propagation time between the two farthest stations. (for 1KM co-axial cable, t=5 µsec).
Performance is greatly improved if frame time is much larger than the propagation time.

## Slide 47: Classic Ethernet (2) – MAC
MAC protocol is 1-persistent CSMA/CD (earlier)
Random delay (backoff) after collision is computed with BEB (Binary Exponential Backoff)
Frame format is still used with modern Ethernet.
Ethernet (DIX)
IEEE 802.3

## Slide 48: Data Link Layer Switching

## Slide 49: Repeater, Hub, Bridge and switch
Repeaters
  They amplify signals
Hub: It has several input lines and joins electrically
  Frames arriving on any of the line are sent to all other lines
  Two frames which arrive same time collide
  Entire hub forms a single Collison domain
Bridge
  Connects two or more LANs
  A software in the bridge examines the destination address and decides where to send the frame
  With a bridge each line is a Collison domain
Switches
  Similar to bridges
  Used to connect several individual computers

## Slide 50: Uses of Bridges
Common setup is a building with centralized wiring
Bridges (switches) are placed in or near wiring closets

## Slide 51: Learning Bridges
A bridge operates as a switched LAN (not a hub)
Computers, bridges, and hubs connect to its ports

## Slide 52: Learning Bridges (2)
Backward learning algorithm picks the output port:
Associates source address on frame with input port
Frame with destination address sent to learned port
Unlearned destinations are sent to all other ports
Needs no configuration
Forget unused addresses to allow changes
Bandwidth efficient for two-way traffic

## Slide 53: Learning Bridges (3)
Bridges extend the Link layer:
Use but don’t remove Ethernet header/addresses
Do not inspect Network header

## Slide 54: Repeaters, Hubs, Bridges, Switches, Routers, & Gateways
Devices are named according to the layer they process
A bridge or LAN switch operates in the Link layer

## Slide 55: Virtual LANs
VLANs (Virtual LANs) splits one physical LAN into multiple logical LANs to ease management tasks
Ports are “colored” according to their VLAN

## Slide 56: Outline
Introduction
Data link layer: An overview
Medium Access layer: An overview
Network layer: An overview
Transport layer: An overview

## Slide 57: Network Layer
Responsible for getting packets from the source to destination through INTERMEDIATE HOPS
Data link layer: only between two points
The network layer deals with end to end transmission
  Should know the topology of the network
  Should not overload some routes and underload other routes.
  Should deal with different networks

## Slide 58
The OSI reference model.

## Slide 59: Design Issues
Store-and-forward packet switching
Connectionless service – datagrams
Connection-oriented service – virtual circuits

## Slide 60: Store-and-Forward Packet Switching
Components of the network layer
  ISP equipment (routers connected by transmission lines)
  Host H1 is directly connected to one of the router
    Home computer plugged into MODEM
    H2 is a LAN, with an office Internet with a router, F, owned and operated by the customer.
    The router has a leased line to the ISP’s equipment.
    F is not part of ISP, but it runs the same algorithms as the ISP’s routers.
The environment of the network layer protocols.
Host sends the packet to the nearest router, which will be forwarded to the next router along the path until it reaches the destination.

## Slide 61: Services Provided to the Transport Layer
Properties of services
  The services should be independent of router technology
  Transport layer should be shielded from the number, type, and topology of the routers present.
  The network addresses made available to transport layer should use a uniform numbering plan across LANs and WANs.
The freedom resulted into two thoughts
  First: Network service should be connectionless with SEND PACKET and RECEIVE PACKET and little more.
    No ordering and flow control should be done.
    Each packet should carry a destination address.
  Second: network should be reliable and connection-oriented service based on the experience of telephone service.
    Without connections, quality of service is difficult to achieve especially for real-time traffic.
First, connectionless service has dominated.
Later, connection-orient service dominated
Currently, both are widely used.

## Slide 62: Connectionless service: datagrams
Packets are injected as datagrams (analogy is telegram).
No advance setup is needed
Network is called datagram network.
  H1 handovers long message to transport layer which instructs to deliver packet to P2 on H2. The transport layer runs in H1 (in the operating system). It prepends transport header and handover it to network layer (another procedure)
Network layer breaks it into packets and sends each of them to router A using point-to-point protocol, PPP.
ISP decides where to send packets. It has to take routing decisions.
The algorithm which does routing decisions are called routing algorithm.
Internet protocol (IP) is the basis of the Internet, individually forwards each packet. 32 bits in IPv4 and 128 bits in IPv6.

## Slide 63: Connectionless Service – Datagrams
Packet is forwarded using destination address inside it
Different packets may take different paths
Routing within a datagram network.

## Slide 64: Connection-oriented: Virtual Circuits
Idea: Avoid having a new route for every packet.
Establish a connection. When a connection is established, the connection set-up is stored in tables.
  The route is used for all traffic flowing over the connection.
H1 established connection 1 with host H2. The first line of A’s table says that if a pack arrives with connection 1 it should be forwarded to C and given connection id as 1.
If H3 also wants to establish a connection to H2, it choses a connection identifier 1 and tells the network to establish a connection.
There is a conflict as A has already used id 1. So, A assigns a different identifier. This process is called label switching. An example of the protocol is MPLS (MultiProtocol label Switching). It wraps packets with 20-bit connection identifier or label.

## Slide 65: Connection-Oriented – Virtual Circuits
Packet is forwarded along a virtual circuit using tag inside it
Virtual circuit (VC) is set up ahead of time
Routing within a virtual-circuit network.

## Slide 66: Comparison of Virtual-Circuits & Datagrams

## Slide 67: Routing Algorithms
The decision has to be made for every packet as best route may be changed over last time.
Network layer design
  Algorithms and data structures
Routing and forwarding
  Forwarding: a process which takes each packet and forwards it to outgoing line.
  Routing: A process which updates the routing tables.
    Routing algorithms play a major role.
Properties of routing algorithm
  Correctness, simplicity:
  Robustness: it should run for years; hosts fail, routers crash, software fails
  Stability: Routing algorithm should converge and reach equilibrium.
  fairness, efficiency

## Slide 68: Routing Algorithms
Shorted Path Routing
Flooding
Distance vector routing
Link state routing
Hierarchical routing
Broadcast routing
Multicast routing

## Slide 69: Congestion Control (1)
Congestion is a situation: Too many packets present in the network causes network delay and loss
Both network and transport layers share the responsibility to control congestion.
Effective way is to reduce the load at the transport layer.
Goodput (=useful packets) trails offered load

## Slide 70: Congestion Control (2)
Network experiences a congestion collapse
If routers will have infinite memory, congestion gets worse
  Packets gets timed out.
Difference between congestion control and flow control
Congestion control is related to whole network. Involves the behavior of all the hosts and routers.
Flow control relates to the traffic between a particular sender and a particular receiver.
Best method is to get host a “slow down”.

## Slide 71: Congestion Control (3) – Approaches
Network must do its best with the offered load
Different approaches at different timescales
Nodes should also reduce offered load (Transport)

## Slide 72: Quality of Service
So far, we have made effort to improve network performance
However, some applications require stronger performance guarantees.
  Example: Multimedia applications:
We will focus of providing network performance with a sharp focus on providing quality of service.
One solution is overprovisioning
  More money is required
With quality of service mechanisms, the network can honor performance guarantees at the cost of turning down some requests.
Issues
  What applications need from the network?
  How to regulate the traffic that enters the network?
  How to reserve the resources at routers to guarantee performance?
  Whether the network can safely accept more traffic
No single technique deals efficiently all these issues..

## Slide 73: Parameters Defining QoS
Throughput/bandwidth - the total amount of work completed during a specific time interval.
Delay - the elapsed time from when a request is first submitted to and when the desired result is produced.
Jitter – Variation in packet arrival times
  Due to lost frames.
  Not acceptable for continuous media applications
  Random variation of transmission time
    Different packets will have different delay
      Disturbs realtime audio and video applications
Reliability/loss - how errors are handled during transmission and processing of continuous media.

## Slide 74: Application Requirements (1)
Different applications care about different properties
We want all applications to get what they need
.
Stringency of applications' quality-of-service requirements.
Application | Bandwidth | Delay | Jitter | Loss
Email | Low | Low | Low | Medium
File sharing | High | Low | Low | Medium
Web access | Medium | Medium | Low | Medium
Remote login | Low | Medium | Medium | Medium
Audio on demand | Low | Low | High | Low
Video on demand | High | Low | High | Low
Telephony | Low | High | High | Low
Videoconferencing | High | High | High | Low

## Slide 75: Application Requirements (2)
Bandwidth:
  E-mail, audio, remote login not need much bandwidth. But file sharing and video in all forms need high bandwidth.
Delay:
  File transfer, email, audio, and video are not delay sensitive. That is if the packets are delayed uniformly across all by a few seconds, no harm is done. So, playing audio or video files from a server does not require low delay.
  But, interactive applications, web access surfing and remote login are more delay sensitive. Telephony, and video conferencing are strictly delay sensitive
.
Jitter
  E-mail, file sharing and web access not sensitive to irregular arrival of packets.
  Remote login is sensitive
  Video and audio are extremely sensitive to Jitter
Loss:
  E-mail, file sharing, web access and remote login have more stringent requirements on loss and bits should be delivered correctly.
  Audio and video applications tolerate lost packets.
    People do not notice short pauses or skipped frames.

## Slide 76: Application Requirements (3)
Network support different categories of QoS
  Constant bit rate (telephony)
    Simulate a wire by providing uniform bandwidth and a uniform delay
  Real-time variable bit rate (e.g., compressed video conferencing)
    Sending a complex frame requires many bits, where a shot of white ball requires less bits.
  Non-real-time variable bit rate (e.g., watching a movie on demand)
    Buffering can be used
  Available bit rate (e.g., file transfer)
    -Use the available bandwidth.
.

## Slide 77: Application Requirements (2)
Network provides service with different kinds of QoS (Quality of Service) to meet application requirements
Network Service | Application
Constant bit rate | Telephony
Real-time variable bit rate | Videoconferencing
Non-real-time variable bit rate | Streaming a movie
Available bit rate | File transfer
Example of QoS categories from ATM networks

## Slide 78: Network Layer in the Internet (1)
IP Version 4 »
IP Addresses »
IP Version 6 »
Internet Control Protocols »
Label Switching and MPLS »
OSPF—An Interior Gateway Routing Protocol »
BGP—The Exterior Gateway Routing Protocol »
Internet Multicasting »
Mobile IP »

## Slide 79: Network Layer in the Internet (2)
IP has been shaped by guiding principles:
Make sure it works
Keep it simple
Make clear choices
Exploit modularity
Expect heterogeneity
Avoid static options and parameters
Look for good design (not perfect)
Strict sending, tolerant receiving
Think about scalability
Consider performance and cost

## Slide 80
Network Layer in the Internet (3)
Internet is an interconnected collection of many networks that is held together by the IP protocol

## Slide 81
IP Version 4 Protocol (1)
IPv4 (Internet Protocol) header is carried on all packets and has fields for the key parts of the protocol:

## Slide 82
IP Version 4 Protocol (1)
Version filed
IHL: header length
Differentiated services: type of service
Total length: every thing in the datagram
Identification field: which packet the newly arrived fragment belong to
  All the fragments of the same packet have the same identification code.
Next field: not defined
DF: do not fragment
MF more fragments
  It is set to know whether all the fragments of datagram have arrived.
Fragment offset
  Where in the current packet this packet belongs
TtL: Time to live
  To limit packet life time
  Decremented after each hop
Protocol: UDP or TCP
Header checksum
Source and destination address indicate the IP address of source and destination
Options field
  For other ideas
  Security
  Strict route
    Set of routes
  Lose routes
    Set of routes

## Slide 83: IP Addresses (1) – Prefixes
Addresses are allocated in blocks called prefixes
Prefix is determined by the network portion
Has 2L addresses aligned on 2L boundary
Written address/length, e.g., 18.0.31.0/24

## Slide 84: IP Addresses (2) – Subnets
Subnetting splits up IP prefix to help with management
Looks like a single prefix outside the network
Network address <Network bits, subnet bits, host bits>
ISP gives network a single prefix
Network divides it into subnets internally

## Slide 85: IP Addresses (3) – Aggregation
Aggregation joins multiple IP prefixes into a single larger prefix to reduce routing table size
ISP advertises
a single prefix
ISP customers have different prefixes

## Slide 86: IP Addresses (5) – Classful Addresing
Old addresses came in blocks of fixed size (A, B, C)
Carries size as part of address, but lacks flexibility
Called classful (vs. classless) addressing

## Slide 87: IP Addresses (6) – NAT
NAT (Network Address Translation) box maps one external IP address to many internal IP addresses
Uses TCP/UDP port to tell connections apart
Violates layering; very common in homes, etc.

## Slide 88: Internet Control Protocols (1)
IP works with the help of several control protocols:
ICMP (Internet Control Message Protocol ) is a companion to IP that returns error info
  Required, and used in many ways, e.g., for traceroute
ARP (Address Resolution Protocol) finds Ethernet address of a local IP address
  Glue that is needed to send any IP packets
  Host queries an address and the owner replies
DHCP (Dynamic Host Configuration Protocol) assigns a local IP address to a host
  Gets host started by automatically configuring it
  Host sends request to server, which grants a lease

## Slide 89
Internet Control Protocols (2)
Main ICMP (Internet Control Message Protocol) types:

## Slide 90
Internet Control Protocols (3)
ARP (Address Resolution Protocol) lets nodes find target Ethernet addresses [pink] from their IP addresses

## Slide 91: Label Switching and MPLS (1)
MPLS (Multi-Protocol Label Switching) sends packets along established paths; ISPs can use for QoS
Path indicated with label below the IP layer

## Slide 92: About IPv6
Support billions of hosts, even with inefficient address space allocation.
Address contains 16 bytes
Notation:
  Written as eight groups of four hexadecimal digits with colons between the groups
  Example: 8000:0000:0000:0000:0123:4567:89AB:CDEF
Optimizations:
  First, leading zeros within a group can be omitted, so 0123 can be written as 123.
  Second, one or more groups of 16 zero bits can be replaced by a pair of colons.
    The above address now becomes 8000::123:4567:89AB:CDEF
  IPv4 addresses can be written as a pair of colons and an old dotted decimal number
    Example ::192.31.20.46